## Slide 1: Numerical Investigation towards a Mechanistic Approach for Prediction of Two-Phase Bubbly Flow with and without Heat and Mass Transfer
Sara Vahaji
First Supervisor: Prof. Jiyuan Tu
Second Supervisor: Dr. Sherman Chi Pok Cheung
Notes: Information to help you understand how the committees work and help you act as a student member.

## Slide 2: Two-phase Bubbly Flow
Source: http://www.youtube.com/watch?v=NXz2CuM2ZZM

## Slide 3: Contents
Introduction
Two-phase bubbly flow without heat and mass transfer
  Numerical modelling
  Case study: bubbly flow over flat plate
Two-phase bubbly flow with heat and mass transfer
  Numerical modelling
  Case study I : subcooled boiling at low pressure
  Case study II: subcooled boiling at elevated pressure
  Conclusion and future work

## Slide 4: Problem Definition

## Slide 5: Transportation Pipelines
Pipelines subjected to long distances
Mineral Processing Pipelines
  Agitate
  Mix
  Effective use of transport momentum
Bubbles generated by
  Gas injection
  Electrolysis

## Slide 6: Application (Safety analysis)
Mass Flow
Source: http://www.youtube.com/watch?v=4bvCDheLm5A

## Slide 7
Two-phase bubbly flow
without
heat and mass transfer

## Slide 8: Two-fluid Model and Closure terms
Two-fluid model: the most practical macroscopic formulation
Closure terms
Turbulent Model
Drag Force and Non-drag Force
Population Balance Model
Turbulent viscosity
Interfacial Force
Interfacial area concentration

## Slide 9: What is Population balance?
Death rate
Birth rate
Ten Years later

## Slide 10: Bubble Size Distribution (BSD)
Number of bubble
Bubble Size
BSD Function
Age
Number of person
Population Distribution

## Slide 11: Bubble Size Distribution (BSD) Equation
PB
DB
ni
ni
PC
DC
ni
ni
if
else
Fluid Velocity
ni
ni
ni
ni
ni
ni’
n’
ni’
ni’
ni’
N(ni)
ni
N(ni)
ni

## Slide 12: MUltiple SIze Group (MUSIG) Model
Used N size group (scalar) to describe bubble population
N extra equations have to be solved (depends on number of group used)
Advantage:
  Higher resolution for bubble classes
Disadvantage:
  Higher computational complexity

## Slide 13: Bubble Coalescence and Breakage
Bubbles may “merge” together forming larger bubbles
Coalescence reduces number of bubbles but increases size of bubbles
N(Dp)
Bubbles may break-up due to turbulence impact
Breakage increases number of bubbles but decrease size of bubbles
N(Dp)
Dp
Dp

## Slide 14: Coalescence Mechanism
Coalescence due to random collisions driven by turbulence
Bounce
Merge

## Slide 15
Research gap:
Influence of different coalescence kernels on BSD
Research questions:
What is the influence of different coalescence kernels on predicting BSD?

## Slide 16: Selected coalescence models
Coalescence kernels:
  Coulaloglou and Tavlarides (1977)- Film drainage model, immobile surface
  Prince and Blanch (1990)-Film drainage model, mobile surface
  Lehr et al. (2002)-critical velocity model
Bounce
Merge
h
Critical thickness
Immobile surfaces
Mobile surfaces
Film drainage model
di
dj
ε

## Slide 17: Computational Geometry
Exp. By Merkle and Deutch
Fig 1- S. Vahaji, L. Chen, S.C.P. Cheung and J.Y. Tu, Modelling of Two-Phase Bubbly Flow over a Flat Plate, 19th Australasian Fluid Mechanics Conference, Melbourne, Australia, Paper No. 55 (Dec. 2014).
Case | Air flow rate Qa (m3/s) | ReL based on the total plate length
Q0-V9.6(Cfo) | 0 | 7.66 x 106
Q1-V9.6 | 0.001 | 7.66 x 106
Q2-V9.6 | 0.0015 | 7.66 x 106
Q3-V9.6 | 0.002 | 7.66 x 106
Q4-V9.6 | 0.0025 | 7.66 x 106

## Slide 18: Boundary Layer Resolution
Fig 2- K. Mohanarangam, S.C.P.Cheung, J.Y. Tu, L.Chen, Numerical simulation of micro-bubble drag reduction using population
balance model, Ocean Engineering Journal, Vol(36), pp. 863–872 (2009).

## Slide 19: Skin-Friction Validation
Cf/Cf0
Qa
Fig 2- S. Vahaji, L. Chen, S.C.P. Cheung and J.Y. Tu, Modelling of Two-Phase Bubbly Flow over a Flat Plate, 19th Australasian Fluid Mechanics Conference, Melbourne, Australia, Paper No. 55 (Dec. 2014).

## Slide 20: Volume Fraction of Air
Fig 3-a- S. Vahaji, L. Chen, S.C.P. Cheung and J.Y. Tu, Modelling of Two-Phase Bubbly Flow over a Flat Plate, 19th Australasian Fluid Mechanics Conference, Melbourne, Australia, Paper No. 55 (Dec. 2014).

## Slide 21: Volume Fraction of Air
Fig 3-b- S. Vahaji, L. Chen, S.C.P. Cheung and J.Y. Tu, Modelling of Two-Phase Bubbly Flow over a Flat Plate, 19th Australasian Fluid Mechanics Conference, Melbourne, Australia, Paper No. 55 (Dec. 2014).

## Slide 22: Bubble Size Distribution
Case Q1-V9.6
Fig 5-a- S. Vahaji, L. Chen, S.C.P. Cheung and J.Y. Tu, Modelling of Two-Phase Bubbly Flow over a Flat Plate, 19th Australasian Fluid Mechanics Conference, Melbourne, Australia, Paper No. 55 (Dec. 2014).
Case Q3-V9.6
Bubble size
Qa

## Slide 23: Without heat and mass transfer: Conclusion and recommendation
Bubbly flow over flat plate successfully simulated using MUSIG model
Influence of different coalescence kernels investigated
It is recommended to test the performance of the model on a real life application (e.g. bubble injection around the body of a ship)

## Slide 24
Two-phase bubbly flow
with
heat and mass transfer

## Slide 25: Phenomenological Description
Subcooled boiling flows are by nature a complex boiling process
Heated walls
Subcooled liquid flows
Coalescence
Bubble nucleation
Condensation
Break-up
Distorted/Cap bubbles
Bubble nucleation
(with sliding)
Single Phase
Subcooled Boiling
Highly Subcooled
Slightly Subcooled
Height
Void Fraction
ONB
NVG

## Slide 26: Phenomenological Observation
Experimental observation by Lee et al., 2002
Bubbles sliding along the heated wall
Bubbles undergoining condensation in the bulk subcooled liquid
Experimental observation by Gopinath et al., 2002
Bubbles merging in the bulk subcooled liquid

## Slide 27: Bubble growth, departure, sliding and lift off
Bubble Condensation
Bubble Growth
Bubble Sliding
Bubble Frequency

## Slide 28: Bubble nucleation
Source: http://www.slis.tsukuba.ac.jp/~fujisawa.makoto.fu/avi/boiling.mp4

## Slide 29
Bubble nucleation
Source: http://www.youtube.com/watch?v=p2NE6o530ak

## Slide 30: Wall Heat Flux Partition Model
Wall heat flux
Quenching (conduction)
Convection
Wall heat flux is divided into three components
Evaporation
Important parameters
Departing Bubble size
Bubble frequency
Active nucleation site density
++

## Slide 31: Empirical correlations for bubble departure diameter
Name | Correlation | Details
Fritz [37] |  | 
Zuber [46] |  | 
Han and Griffith [38] |  | 
Cole and Shulman [35] |  | 
Cole [33] |  | 
Cole and Rohsenow [34] |  | 
Tolubinskiy and Kostanchuk [41] |  | 
Unal [42] |  | 
Kocamustafaogullari and Ishii [18] |  | 
Farajisarir [36] |  | 
Morel et al. [40] |  | 
Table 2- S.C.P. Cheung, S. Vahaji, G.H. Yeoh and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 1: Assessment of empirical correlations, International Journal of Heat and Mass Transfer, Vol(75), pp. 736-753 (2014). Journal Rank: A*

## Slide 32: Empirical correlations for bubble frequency
Name | Correlation | Details
Cole [50] |  | 
Zuber [46] |  | 
Hatton and Hall [51] |  | 
Ivey [52] |  | for hydrodynamic region
 |  | for transition region
 |  | for thermodynamic region
Stephan [53] |  | 
Kocamustafaogullari and Ishii [55] |  | 
Podowski et al. [56] |  | 
Table 3- S.C.P. Cheung, S. Vahaji, G.H. Yeoh and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 1: Assessment of empirical correlations, International Journal of Heat and Mass Transfer, Vol(75), pp. 736-753 (2014). Journal Rank: A*

## Slide 33: Empirical correlations for active nucleation site density
Author | Correlation | Details | 
Gaertner and Westwater [15] |  | m = 0.48 | 
Hsu and Graham [25] |  |  | 
 |  | 0.48 < m < 1 | 
Kirby and Westwater [26] |  |  | 
 |  | m = 0.73 (glass), 0.48 < m < 1 (metal) | 
Mikic and Rohsenow [22] |  |  | 
 |  |  | m =3, C=4×10-12
Johov [17] |  |  | 
Bier [13] |  | m = 0.42 (Freon-115) m = 0.26 (Freon-11) | 
Cornwel and Brown [14] |  | m = 4.5 | 
Lemmert and Chawla [21] |  | n = 185 , m = 1.805 | 
Koncar et al. [19] |  | n = 210 , m = 1.805 | 
Kurul and Podowski [9] |  |  | 
Krepper et al. [27, 28] |  | n = 0.8×106, ΔTrefN =10K (exp. of Bartolomej) n = 3×107 (exp.s of DEBORA 1-2) n = 5×106 (exp.s of DEBORA 3-7) | 
Kocamustafaogullari and Ishii [18] |  |  | 
Wang and Dhir [23] |  |  | 
Benjamin and Balakrishnan [12] |  |  | 
Hibiki and Ishii [16] |  |  | 
Basu, Warrier and Dhir [11] |  | ΔTONB <Tsup< 15 K | 
 |  | Tsup ≥ 15 K | 
Table 1- S.C.P. Cheung, S. Vahaji, G.H. Yeoh and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 1: Assessment of empirical correlations, International Journal of Heat and Mass Transfer, Vol(75), pp. 736-753 (2014). Journal Rank: A*

## Slide 34
Research gap:
Highly empirical correlations for prediction of bubble dynamics (D,f,Na)
Sliding of the bubbles on the wall is not considered
Research questions:
How to adopt a more mechanistic model for prediction of bubble dynamics?
How to mechanistically predict the bubble detachment diameter,
bubble departure frequency, and
active nucleation site density?
If possible, how to couple the mechanistic models with two-fluid model?
If possible, how would it perform compared to existing empirical correlations?

## Slide 35: Force Balance Model for Bubble Detachment
Fx = Fsx + Fdux + FsL + Fh + Fcp
Fy = Fsy + Fduy + Fqs + Fb
Fig 2- G.H. Yeoh et al., Fundamental consideration of wall heat partition of vertical subcooled boiling flows, Int. J. Heat Mass Transfer, Vol(51), pp. 3840–3853 (2008).
The forces acting on the bubble are:
  surface tension force (Fs)
  unsteady drag force due to asymmetrical growth of the bubble (Fdu)
  shear lift force (FsL)
  force due to the hydrodynamic pressure (Fh)
  contact pressure force accounting for the bubble being in contact with a solid (Fcp)
  quasi steady-drag force in the flow direction (Fqs)
  buoyancy force (Fb)

## Slide 36: Force Balance Model for Bubble Detachment (con’t)
The forces acting on the bubble in the x- and y-directions are:
Fx = Fsx + Fdux + FsL + Fh + Fcp
Fy = Fsy + Fduy + Fqs + Fb
Along the x-direction Along the y-direction
,  and i are the advancing, receding and inclination angles respectively; dw is the surface/bubble contact diameter

## Slide 37: Bubble Frequency
Growth time tg is evaluated directly from the force balance model for the bubble lift-off
Waiting time tw is determined according to
Cavity Radius
F indicates the degree of flooding of the available cavity size and the wettability of the surface

## Slide 38: Bubble growth, sliding and lift-off
Lift-off
Heated Surface
Atc
Qtc
Qc
Dl
Fluid direction
Sliding
Qtcsl
Qc
Atcsl
Dsl
Heated Surface
Fluid direction
Growth
Qe
Qe
Qc
Heated Surface
Fluid direction
Fig 1- G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*

## Slide 39: Improved Wall Heat Flux Partition Model
Wall heat flux
Transient conduction due to stationary bubbles
Transient conduction due to sliding bubbles
Convection
Wall heat flux is divided into four components
Evaporation
Important parameters
Active nucleation site density
Departing Bubble size
Bubble frequency

## Slide 40: Fractal Model
Formulation:
Fractal scaling law cumulative number of active cavities greater than and equal to particular cavity diameter Dc is given by
Maximum diameters of active cavity
Minimum diameters of active cavity
Fractal dimension
Thermal boundary layer thickness

## Slide 41: Physical Modeling Considerations:
Transportation of both phases two-fluid model
Bubble coalescence and break-up population balance model (MUSIG)
Condensation in subcooled liquid source term to liquid phase
Bubble departure and lift-off diameter
(Dd, Dsl, Dl)
Bubble departure frequency (f)
Active nucleation site density (Na)
Wall boundary condition;
Source term for gas phase;
Source term for energy equation

## Slide 42: Case study I: subcooled boiling at low pressure
Local case
Exp. By Prof Park and colleagues
Experimental conditions
Case | Pinlet [MPa] | Tinlet [oC] | Tsub (inlet) [oC] | Qw [kW/m2] | G [kg/m2s]
L1 | 0.143 | 96.9 | 13.4 | 152.9 | 474.0
L2 | 0.137 | 94.9 | 13.8 | 197.2 | 714.4
L3 | 0.143 | 92.1 | 17.9 | 251.5 | 1059.2
19 mm
1670 mm long Heated Section
9.25 mm
Inlet Liquid Flow
Heated Inner Tube
Measuring Plane
at
1610 mm

## Slide 43: Case study I (cont’d)
Axial case
Exp. by Zeitoun & Shoukri
Experimental conditions
Case | Pinlet [MPa] | Tinlet [oC] | Tsub (inlet) [oC] | Qw [kW/m2] | G [kg/m2s]
A1 | 0.137 | 91.9 | 14.9 | 286.7 | 156.2
A2 | 0.122 | 93.6 | 11.6 | 286.5 | 258.2
A3 | 0.150 | 94.6 | 16.6 | 508.0 | 264.3
A4 | 0.150 | 88.9 | 22.5 | 705.0 | 411.7
12.7 mm
306 mm long Heated Section
Inlet Liquid Flow
Heated Inner Tube
25.4 mm

## Slide 44: Void Fraction Distribution
Fig 8- G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*
Fig 7- G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*
higher void fraction close to heated wall
Bubbles condense as get exposed to subcooled liquid
higher void fraction close to the exit

## Slide 45: Nucleation site density distribution
Fig 4- G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*
Fig 3- G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*

## Slide 46: Nucleation Site Density vs. Superheat Temperature
LC predicts higher Na compared to Basu
Fig 12- G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 1: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 736-753 (2014). Journal Rank: A*

## Slide 47: Wall superheat temperature
Fig 12- G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*
Fig 11- G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*

## Slide 48: Bubble departure frequency
Increasing bubble frequency along the heated wall as expected from physical mechanisms

## Slide 49: Contribution of conduction heat
Fig 14- G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*
Fig 13- G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*
High conduction due to sliding bubbles
Empirical correlations don’t pick enough quenching for radial case
Consistent prediction for both axial and radial cases

## Slide 50: Case study II: subcooled boiling at elevated pressure
Exp. by Ozar et al.
Experimental conditions
Case | Pinlet [MPa] | Tinlet [oC] | Tsub (inlet) [oC] | Qw [kW/m2] | G [kg/m2s]
M1 | 0.218 | 110.3 | 12.7 | 237.9 | 1843.8
M2 | 0.497 | 136.7 | 14.8 | 190.9 | 942.3
M3 | 0.949 | 167.6 | 10.0 | 208.5 | 964.4
19.1 mm
2.8 m long Heated Section
Inlet Liquid Flow
Heated Inner Tube
38.1 mm
1.7 m long
Non-Heated Section
Measuring Plane
at
2.05 m

## Slide 51: Radial Void Fraction Distribution at 2.05m

## Slide 53: Influence of pressure – empirical model

## Slide 54: Influence of pressure – mechanistic model

## Slide 55: Conclusion
A more mechanistic approach for bubble frequency, departure and lift-off diameter, and active nucleation site density is presented
Some empirical correlations yield better prediction with axial condition but are not good for local condition
The mechanistic model is capable of capturing underlying physics
Transient conduction due to sliding bubbles becomes the dominant heat transfer mode
Mechanistic model could cover a wide range of fluid conditions consisting of wall heat flux, inlet velocity, inlet subcooling temperature, and pressure

## Slide 56: Future work
Other fluids
A more mechanistic approach for prediction of bubble growth rate in force balance model
More precise model for better handling bubble induced turbulence
Packing behavior of neighbouring bubbles
Different coalescence and break-up kernels

## Slide 57: Acknowledgement:
ARC Linkage Project (LP0990691) and Green Earth Energy Ltd.
ARC Discovery Project (DP130100819)
Defence Science and Technology Organisation (DSTO)

## Slide 58: All Publications:
Refereed Journal Articles:
S. Vahaji, S.C.P. Cheung, G.H. Yeoh and J.Y. Tu, Investigation of the Influence of Elevated Pressure on Subcooled Boiling Flow - Evaluation of Mechanistic Approach, AIChE Journal, (Under Review) (2015). Journal Rank: A*
A. Date, S. Vahaji, J. Andrews and A. Akbarzadeh, Experimental performance of a rotating two-phase reaction turbine, Applied Thermal Engineering, Vol. 76, pp. 475-483 (2015). Journal Rank: A*
G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*
S.C.P. Cheung, S. Vahaji, G.H. Yeoh and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 1: Assessment of empirical correlations, International Journal of Heat and Mass Transfer, Vol(75), pp. 736-753 (2014). Journal Rank: A*
S. Vahaji, A. Akbarzadeh, A. Date, S.C.P. Cheung and J.Y. Tu, Efficiency of a two-phase nozzle for geothermal power generation, Applied Thermal Engineering, Vol. 73, pp. 227-235 (2014). Journal Rank: A*
S. Vahaji, A. Date, S.C.P. Cheung, J.Y. Tu, A. Akbarzadeh and M. Oreijah, Experimental analysis of two-phase flow nozzle for desalination and power generation system, Proceedia Engineering, Vol. 49, pp. 324-329 (2012).
Refereed Conference Papers:
S. Vahaji, L. Chen, S.C.P. Cheung and J.Y. Tu, Modelling of Two-Phase Bubbly Flow over a Flat Plate, 19th Australasian Fluid Mechanics Conference, Melbourne, Australia, Paper No. 55 (Dec. 2014).
S. Vahaji, S.C.P. Cheung, G.H. Yeoh and J.Y. Tu, Modeling Subcooled Boiling Flow in Low and Medium Pressures – Evaluation of Mechanistic Approach, OECD/NEA & IAEA Workshop, CFD4NRS-5, Application of CFD/CMFD Codes to Nuclear Reactor Safety and Design and their Experimental Validation, Zurich, Switzerland (Sep. 2014).
S. Vahaji, A. Akbarzadeh, A. Date, S.C.P. Cheung and J.Y. Tu, The efficiency of a two-phase nozzle as a motive force for power generation from low temperature resources, Heat Transfer 2014, A Coruna, Spain, Vol. 83 of WIT Transactions on Engineering Sciences, (Jul 2014).
S. Vahaji, S.C.P. Cheung, G.H. Yeoh and J.Y. Tu, Towards a mechanistic model for subcooled flow boiling at low pressure, CFD 2014, Trondheim, Norway, Paper No. 045 (Jun 2014).

## Slide 59
THANK YOU

## Slide 61: Breakage Mechanism
Breakage due to the impact of turbulent eddies
Impact by turbulent eddies
Unaffected
Uneven breakage due to fluid shearing
Even breakage

## Slide 62: Bubble Size Distribution – break-up coefficient = 0.05
Case Q1-V9.6
Fig 4- S. Vahaji, L. Chen, S.C.P. Cheung and J.Y. Tu, Modelling of Two-Phase Bubbly Flow over a Flat Plate, 19th Australasian Fluid Mechanics Conference, Melbourne, Australia, Paper No. 55 (Dec. 2014).
Bubble size
Qa
Case Q3-V9.6

## Slide 63: Wall Heat Flux Partition Flowchart
Fig 2 G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*

## Slide 64: Transient Conduction
Fractal model for stationary bubbles
Fractal model for sliding bubbles
Waiting time
Sliding time
Departure diameter
Average diameter (Dd +Dl)/2 where Dl is the lift-off diameter

## Slide 65: Other Wall Heat Flux Components
Fractal model for evaporation
Fractal model for convection
Reduction factor – ratio of actual number of bubbles lifting off to the number of active nucleation sites
d = 2 for 2D space
Lift-off diameter
Area of influence

## Slide 66: Results and Discussion
Local comparison
Local measurements at 1.61 m downstream of the beginning of the heated section (near the flow exit)
Homogeneous Multiple Size Group (MUSIG) model
15 classes between 0 mm and 8.5 mm

## Slide 67: Results and Discussion (con’t)
Axial comparison
Axial measurements
Homogeneous Multiple Size Group (MUSIG) model
15 classes between 0 mm and 6.0 mm

## Slide 68: Results and Discussion
Elevated pressure comparison
Local measurement 2.05 m downstream of the beginning of the heated section
Homogeneous Multiple Size Group (MUSIG) model
15 classes between 0 mm and 6.35 mm

## Slide 69: Frequency distribution
Fig 6 G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*

## Slide 70: Frequency distribution
Fig 5 G.H. Yeoh, S. Vahaji, S.C.P. Cheung and J.Y. Tu, Modelling Subcooled Flow Boiling in Vertical Channels at Low Pressures - Part 2: Evaluation of Mechanistic Approach, International Journal of Heat and Mass Transfer, Vol(75), pp. 754-768 (2014). Journal Rank: A*

## Slide 72: Radial Interfacial Area Concentration Distribution at 2.05m

## Slide 73: Radial Bubble Sauter Mean Diameter Distribution at 2.05m

## Slide 74: Transient Conduction
Heat transfer due to sliding and stationary bubbles:
latent heat transfer due to microlayer evaporation
transient conduction during the waiting period
Stationary bubble: point of inception
Sliding bubble: area occupied by the sliding bubble at any instant of time and regions being swept by sliding bubbles

## Slide 75: Fractal Model (con’t)
Formulation:
df for a boiling system:
Averaged over maximum active cavities
Constant value = 0.1oC

## Slide 76: Three-dimensional Two-Fluid Model
Continuity Equation:
Liquid Phase
Gas Phase

## Slide 77: Three-dimensional Two-Fluid Model (con’t)
Momentum Equation:
Interphase Momentum Transfer
where

## Slide 78: Three-dimensional Two-Fluid Model (con’t)
Energy Equation:
Interphase Heat Transfer
where
Sauter Mean Diameter
Interfacial heat transfer

## Slide 79: Axial bubble Sauter mean diameter distribution
Bigger bubble size close to the exit

## Slide 80: Radial bubble Sauter mean diameter distribution
bigger size close to heated wall due to coalescence
Bubbles condense as get exposed to subcooled liquid

## Slide 81: Influence of pressure on Na and f